## Slide 1: Differential Fault Analysis on AES Variants
Kazuo Sakiyama, Yang Li
The University of Electro-Communications
2012-8-29 @ Nagoya, Japan

## Slide 2: Contents
Background
  Physical Attacks and Differential Fault Analysis
  Advanced Encryption Standard
  Fault Model in this discussion
    1-byte random fault in known byte position
DFA Attack on AES Variants
  DFA on AES-128 with 1 fault injection
  DFA on AES-192 with 3/2 fault injections
  DFA on AES-256 with 3/2 fault injections
    Challenge to be practically feasible
Conclusion

## Slide 3: Cryptanalytic Attacks
Mathematical Approach
Physical Approach
  Keep the proposed attack feasible
=?
Physical
Information Channels
Input
Output
Cryptographic device
(Secret key inside)
Input
Output
=?
Input
Output
Notes: There are certain cryptanalytic attacks that are trying to recover the secret key. These attacks can be largely divided into 2 types.

## Slide 4: Classification of Physical Attacks
Direction of information channel
=?
Cryptographic device
(Secret key inside)
Input
Output
Passive Attacks
Active Attacks
Input, Output Known
Non-Invasive Passive Attacks
(Side-Channel Analysis)
Time,
Power Consumption,
Electromagnetic Radiation
Non-Invasive Active Attacks
(Fault Analysis)
Inject computational faults
Notes: Passive Attacks
(Side-Channel Analysis)

## Slide 5: Differential Fault Analysis (DFA) on AES Encryption
DFA (Most discussed fault analysis)
Attack Procedures
P
AES
AES
C’
C
II’
I
ΔI = I I’
C’
C
Key Guess: Kg
AES Decryption
AES Decryption
Kg-based Correct
Intermediate Value: Ig
Kg-based Faulty
Intermediate Value: I’g
ΔIg
ΔI
Match?
P
Fault Model: Space of ΔI
e.g. 1-byte random fault at a known byte position
Notes: Correct Intermediate Value based on Kｇ： Iｇ

## Slide 6: Advanced Encryption Standard
Substitution permutation network
Symmetric algorithm
128-bit input block
3 versions
  128-bit key (10 Rounds)
  192-bit key (12 Rounds)
  256-bit key (14 Rounds)
SB
SR
MC
AK
AES Round Operation

## Slide 7: AES Key Schedule
F
K0
K1
… …
K10
AES-128
F
K0
… …
K12
AES-192
K1
K2

## Slide 8: AES Key Schedule
F
… …
K13
AES-256
Sub
Word
K0
K1
K3
K2
K14
Notes: The knowledge of two consecutive subkeys allows to recover the entire key for AES-192 and for AES-256.
Two rounds of AES achieve a full diffusion for all keysize variants of AES.

## Slide 9: Fault Model in this presentation
Fault model:
  1-byte random fault model
  Random faulty value at a known byte position
  1 S-box calculation has a faulty result
Fault injection based on setup-time violation
  Clock glitch
  Less time for a certain clock cycle (round operation)

## Slide 10: DFA attacks on AES Variants
The minimal times of fault injections but still within a practical key recovery complexity
DFA on AES-128 with 1 fault injection
  CHES03, Africa09, WISTP11
DFA on AES-192 with 3 fault injections
  FDTC11
DFA on AES-256 with 3 fault injections
  FDTC11
DFA on AES-192 with 2 fault injections
  Improved a little from FDTC11
DFA on AES-256 with 2 fault injections
  IEEE Trans. on Info. F&S

## Slide 11: DFA on AES-128
SB8
SR8
MC8
AK8
SB9
3
4
1
2
SR9
3
4
1
2
MC9
1
4
2
3
1
4
2
3
1
4
2
3
1
4
2
3
AK9
SB10
SR10
AK10
1
4
2
3
1
4
2
3
1
4
2
3
1
4
2
3
1
4
2
3
1
4
2
3
1
4
2
3
1
4
2
3
3
2
4
1
2
1
3
4
1
4
2
3
4
3
1
2
C
C’
2-8
23228
23228
23228
23228
2128
28
20
Without considering K9, we can reduce K10 space to 232

## Slide 12: DFA Attacks on AES-192 (simple attack, 3 faults)
SB9
SR9
MC9
AK9
SB10
SR10
MC10
AK10
SB11
SR11
MC11
AK11
SB12
SR12
AK12
C1
C1’
SB9
SR9
MC9
AK9
SB10
SR10
MC10
AK10
SB11
SR11
MC11
AK11
SB12
SR12
AK12
C2
C2’
SB9
SR9
MC9
AK9
SB10
SR10
MC10
AK10
SB11
SR11
MC11
AK11
SB12
SR12
AK12
C3
C3’
Identify K12 first using (C1,C1’) and (C1,C2’), then recover K11

## Slide 13: DFA Attacks on AES-256 (simple attack, 3 faults)
SB11
SR11
MC11
AK11
SB12
SR12
MC12
AK12
SB13
SR13
MC13
AK13
SB14
SR14
AK14
C1
C1’
SB11
SR11
MC11
AK11
SB12
SR12
MC12
AK12
SB13
SR13
MC13
AK13
SB14
SR14
AK14
C3
C3’
SB11
SR11
MC11
AK11
SB12
SR12
MC12
AK12
SB13
SR13
MC13
AK13
SB14
SR14
AK14
C2
C2’
Identify K14 first using (C1,C1’) and (C1,C2’), then recover K13

## Slide 14: Maybe 2 faults are enough for AES-192 and AES-256
Space of Kg
C’
C
Key Guess: Kg
AES Decryption
AES Decryption
Kg-based Correct
Intermediate Value: Ig
Kg-based Faulty
Intermediate Value: I’g
ΔIg
ΔI
Match?
Space of ΔI
Satisfy zero-difference bytes
in intermediate status
AES 128: 128-bit  8-bit
AES 192: 192-bit  72-bit  0 bit
AES 256: 256-bit  136-bit  16-bit
  Keep the proposed attack feasible!

## Slide 15: DFA Attacks on AES-192 (2 faults)
SB9
SR9
MC9
AK9
SB10
SR10
MC10
AK10
SB11
SR11
MC11
AK11
SB12
SR12
AK12
C1
C1’
SB9
SR9
MC9
AK9
SB10
SR10
MC10
AK10
SB11
SR11
MC11
AK11
SB12
SR12
AK12
C2
C2’
Restrict K12 to 232

## Slide 16: Some property for AES-192 key Schedule
F
K10
K12
AES-192
K11
For AES-192:
K12left 2 columns of K11
K12right 1 column of K10

## Slide 17: DFA Attacks on AES-192 (2 faults)
SB9
SR9
MC9
AK9
SB10
SR10
MC10
AK10
SB11
SR11
MC11
AK11
SB12
SR12
AK12
C1
C1’
SB9
SR9
MC9
AK9
SB10
SR10
MC10
AK10
SB11
SR11
MC11
AK11
SB12
SR12
AK12
C2
C2’
Restrict K12 to 232
Given a K12 candidate, leftmost 2 columns of K11 is fixed, we have 5 more 2-8 conditions to satisfy. So we can identify K12
Identify the rest of K11
SB11
SR11
MC11
AK11
MC10
AK10
SB11
SR11
MC11
AK11
MC10
AK10

## Slide 18: DFA Attacks on AES-256 (2 faults)
Restrict K14 to 232
SB11
SR11
MC11
AK11
SB12
SR12
MC12
AK12
SB13
SR13
MC13
AK13
SB14
SR14
AK14
C2
C2’
SB11
SR11
MC11
AK11
SB12
SR12
MC12
AK12
SB13
SR13
MC13
AK13
SB14
SR14
AK14
C1
C1’

## Slide 19: AES S-box Differential Table
For an AES S-box, given a pair of input/output difference, this difference exists with probability of about ½. If this difference pair exist, one can find 2 pairs of solution.
Given N pairs of input/output difference, we can expect N real value solutions
Used in the inbound of Rebound Attack
Outbound Inbound Outbound

## Slide 20: Some property for AES-256 key Schedule
F
AES-256
K12
K13
K14
For AES-256:
K12right 3 columns of K12

## Slide 21: DFA Attacks on AES-256 (2 faults)
Restrict K14 to 232
Pick up a K14, calculate the difference at SB13out, and restrict real values in each column to 28
Then we know the rightmost 3 columns of K12, calculate the blue bytes in SB12in, check 2 conditions of 2-8. Space of SB13out is reduced to 216. Then K13 is reduced to 216
(Complexity about 248, key recovery using FPGA takes 8 days to finish)
MC12
AK12
SB13
SR13
SB11
SR11
MC11
AK11
SB12
SR12
MC12
AK12
SB13
SR13
MC13
AK13
SB14
SR14
AK14
C2
C2’
SB11
SR11
MC11
AK11
SB12
SR12
MC12
AK12
SB13
SR13
MC13
AK13
SB14
SR14
AK14
C1
C1’
MC12
AK12
SB13
SR13
SR12
SB12
AK11
MC11

## Slide 22: Conclusion
In side-channel attacks especially fault analysis, cryptanalysis techniques can help.
For AES-256, DFA attack with two 1-byte random faults at known position are feasible for strong attackers
Can we make DFA with unknown positions faults feasible?

## Slide 23: Thank you for your attentions!